## Slide 1
CHARUSAT
IEEE Student Branch
|
“A Student Chapter of the IEEE Circuits and Systems Society“
2. Introduction
1.Objective
3. Methodology
5. Simulation Results
6. Conclusion and future scope
Prepared by:
Mentored by:
Dr.Arpita Patel
Kushal Pitaliya
ID NO. 23EC105
Course : “ EC317 - Modeling Using Verilog ”
Design and Implementation of an 8-bit Synchronous FIFO on a Spartan-6 FPGA
Associate Professor, EC Dept
The primary objective of this project is to design, simulate, implement, and physically verify an 8-bit wide, 16-word deep synchronous First-In-First-Out (FIFO) memory buffer. The design will be coded in Verilog HDL and implemented on an EDGE Spartan 6 FPGA board. The project aims to demonstrate a robust, real-time hardware system for digital data queuing, complete with status indicators for full and empty conditions, controlled and monitored using physical switches and LEDs.
The project followed a structured FPGA design and verification flow:
Design using Verilog HDL: A modular design approach was adopted with three key modules:
fifo_sync.v (Core Logic): This module implements the heart of the FIFO. It contains the 8-bit memory array, separate read and write pointers, and an item_count register to robustly manage the full and empty status flags. The output is registered to ensure a clean, stable data signal.
debounce.v (Button Filter): This crucial utility module takes a noisy physical button press as input and, using a timer-based filter, produces a single, clean, one-clock-cycle pulse. This prevents a single press from being incorrectly registered multiple times.
top_fifo.v (Hardware Interface): This top-level module integrates the system. It instantiates the fifo_sync core and three separate instances of the debounce module (for Write, Read, and Reset). It also includes a power-on reset circuit to ensure the FIFO initializes correctly.
Simulation in Xilinx ISE: A Verilog testbench was used to rigorously test the complete design, including the debouncer, to verify all logical behaviors and boundary conditions before synthesis.
Synthesis and Implementation: The Verilog design was synthesized into a gate-level netlist using the Xilinx ISE tool. The Implement step then performed Place & Route, mapping the logic onto the Spartan-6 fabric and generating the final .bit file.
Hardware testing and output observation: The .bit file was downloaded to the EDGE Spartan 6 board. Functionality was verified by setting data on slide switches, using the three push buttons, and observing the output on the data and status LEDs.
UCF file intro: The top_fifo.ucf (User Constraints File) was created to map the port names from top_fifo.v to the physical pins of the FPGA, such as NET "clk_50mhz" LOC = "P84";.
Note on Frequency Division: This project operates entirely on the board's single 50 MHz system clock. Frequency division was not required, as all operations are synchronous to the main clock, and the debounce module uses a counter to manage timing delays rather than generating a new, continuous clock signal.
Conclusion: This project successfully demonstrates the end-to-end design, simulation, and hardware implementation of a robust 8-bit synchronous FIFO on a Spartan-6 FPGA. The successful verification on physical hardware confirms a solid understanding of digital memory design, state machine logic, and interfacing with real-world I/O. The inclusion of power-on reset and button debouncing logic ensures the design is stable and reliable.
Future Enhancements:
Asynchronous FIFO: The next logical step would be to implement an asynchronous FIFO, which uses two independent clocks for writing and reading.
UART Interface Integration: Integrate a UART (Universal Asynchronous Receiver/Transmitter) module to allow data to be sent to the FIFO from a PC and read back to a serial terminal.
Parameterized Scalability: The current design uses parameters for data width and address width. A future step could be to test the design's scalability by synthesizing it with different parameters (e.g., a 32-bit wide, 256-word deep FIFO) to analyze the impact on resource utilization.
A First-In-First-Out (FIFO) is a vital digital logic block that functions as a memory buffer, enforcing a "first-in, first-out" data processing order. It serves as an elastic buffer between two communicating systems, particularly useful for rate matching (buffering data between a fast producer and a slow consumer) or for handling data bursts.
This project focuses on a synchronous FIFO, where both the write and read operations are controlled by the same clock signal. Implementing this design on a Field-Programmable Gate Array (FPGA) is ideal because it allows for rapid prototyping and tangible, real-time hardware verification. The FPGA's reconfigurable nature enables us to directly interact with the digital circuit using physical I/O, providing a powerful platform for validating the design's functionality beyond software simulation.
4. Components
  Hardware:
      FPGA: Xilinx Spartan-6 (XC6SLX9-TQG144C) on an EDGE Spartan 6 Development Board.
      Clock Source: 50 MHz crystal oscillator.
      Input Devices: 8 SPDT slide switches for parallel data input; 3 tactile push buttons for Write, Read, and Reset control (active-high).
      Output Devices: 8 general-purpose LEDs for data output; 2 additional LEDs for full and empty status indication.
      USB JTAG Programmer: The interface for downloading the compiled bitstream file to the FPGA.
      5V Power Supply: Provides power to the FPGA board.
  Software:
      Design Suite: Xilinx ISE 14.7.
      Programming Tool: Xilinx iMPACT.
      Hardware Description Language: Verilog.
5. Simulation Result
The project's logical correctness was confirmed through simulation, and the overall methodology followed the standard FPGA design flow, as illustrated in the flowchart below. This structured process ensures that the design is verified in software before being committed to hardware.
Verification through Simulation
Before synthesis, the system was thoroughly simulated using a Verilog testbench in Xilinx ISE. The simulation confirmed that the design logic performed exactly as intended:
Reset Functionality: The testbench verified that a reset pulse correctly initializes the FIFO to a known empty state, causing the empty flag to assert.
FIFO Operation: A sequence of data was written into the FIFO, followed by a sequence of reads. The simulation confirmed that data was read out from the output port in the exact same sequence it was written, proving correct First-In, First-Out behavior.
Status Flags: The empty and full flags were verified to assert and de-assert correctly at their respective boundary conditions, preventing data underflow and overflow.
The hardware performed exactly as the simulation predicted, successfully validating the entire design from code to the physical chip.